## Slide 1
Tropospheric Emissions: Monitoring of Pollution
(TEMPO) – status and
potential science studies
Kelly Chance
Smithsonian Astrophysical
Observatory
May 11, 2016

## Slide 2: Hourly atmospheric pollution from geostationary Earth orbit
PI: Kelly Chance, Smithsonian Astrophysical Observatory
Instrument Development: Ball Aerospace
Project Management: NASA LaRC
Other Institutions: NASA GSFC, NOAA, EPA, NCAR, Harvard, UC Berkeley, St. Louis U, U Alabama Huntsville, U Nebraska, RT Solutions, Carr Astronautics
International collaboration: Korea, U.K., ESA, Canada, Mexico, Cuba, Spain
Selected Nov. 2012 as NASA’s first Earth Venture Instrument
  Instrument delivery May 2017
  NASA will arrange hosting on commercial geostationary communications satellite with launch expected NET 11/2018
Provides hourly daylight observations to capture rapidly varying emissions & chemistry important for air quality
  UV/visible grating spectrometer to measure key elements in tropospheric ozone and aerosol pollution
  Distinguishes boundary layer from free tropospheric & stratospheric ozone
Aligned with Earth Science Decadal Survey recommendations
  Makes many of the GEO-CAPE atmosphere measurements
  Responds to the phased implementation recommendation of GEO-CAPE mission design team
  North American component of an international constellation for air quality observations

## Slide 3: TEMPO instrument concept
Measurement technique
  Imaging grating spectrometer measuring solar backscattered Earth radiance
  Spectral band & resolution: 290-490 + 540-740 nm @ 0.6 nm FWHM, 0.2 nm sampling
  2 2-D, 2k×1k, detectors image the full spectral range for each geospatial scene
Field of Regard (FOR) and duty cycle
  Mexico City/Yucatan, Cuba to the Canadian oil sands, Atlantic to Pacific
  Instrument slit aligned N/S and swept across the FOR in the E/W direction, producing a radiance map of Greater North America in one hour
Spatial resolution
  2.1 km N/S × 4.7 km E/W native pixel resolution (9.8 km2)
  Co-add/cloud clear as needed for specific data products
Standard data products and sampling rates
  Most sampled hourly, including eXceL O3 (troposphere, PBL)
  NO2, H2CO, C2H2O2, SO2 sampled hourly (average results for ≥ 3/day if needed)
  Nominal spatial resolution 8.4 km N/S × 4.7 km E/W at center of domain (can often measure 2.1 km N/S × 4.7 km E/W)
  Measurement requirements met up to 50o for SO2, 70o SZA for other products

## Slide 4: Typical TEMPO-range spectra (from ESA GOME-1)

## Slide 5: Baseline and threshold data products
Species/Products | Required Precision | Temporal Revisit
0-2 km O3 (Selected Scenes) Baseline only | 10 ppbv | 2 hour
Tropospheric O3 | 10 ppbv | 1 hour
Total O3 | 3% | 1 hour
Tropospheric NO2 | 1.0 × 1015 molecules cm-2 | 1 hour
Tropospheric H2CO | 1.0 × 1016 molecules cm-2 | 3 hour
Tropospheric SO2 | 1.0 × 1016 molecules cm-2 | 3 hour
Tropospheric C2H2O2 | 4.0 × 1014 molecules cm-2 | 3 hour
Aerosol Optical Depth | 0.10 | 1 hour
Minimal set of products sufficient for constraining air quality
Across Greater North America (GNA): 18°N to 58°N near 100°W, 67°W to 125°W near 42°N
Data products at urban-regional spatial scales
  Baseline ≤ 60 km2 at center of Field Of Regard (FOR)
  Threshold ≤ 300 km2 at center of FOR
Temporal scales to resolve diurnal changes in pollutant distributions
Collected in cloud-free scenes
Geolocation uncertainty of less than 4 km
Mission duration, subject to instrument availability
  Baseline 20 months
  Threshold 12 months

## Slide 6: TEMPO mission concept
Geostationary orbit, operating on a commercial telecom satellite
  NASA will arrange launch and hosting services (per Earth Venture Instrument scope)
    80-115o W acceptable latitude
    Specifying satellite environment, accommodation
  Hourly measurement and telemetry duty cycle for at least ≤70o SZA
TEMPO is low risk with significant space heritage
  We proposed SCIAMACHY in 1985, as suggested by the late Dr. Dieter Perner
  All proposed TEMPO measurements have been made from low Earth orbit satellite instruments to the required precisions by SAO and Science Team members
  All TEMPO launch algorithms are implementations of currently operational algorithms
    NASA TOMS-type O3
    SO2, NO2, H2CO, C2H2O2 from fitting with AMF-weighted cross sections
    Absorbing Aerosol Index, UV aerosol, Rotational Raman scattering cloud
    SAO eXceL profile/tropospheric/PBL O3 for selected geographic targets
Example higher-level products: Near-real-time pollution/AQ indices, UV index
TEMPO research products will greatly extend science and applications
  Example research products: BrO and IO from AMF-normalized cross sections; height-resolved SO2; additional cloud/aerosol products; vegetation products; additional gases

## Slide 7: Geostationary orbit opportunities of interest
TEMPO can be located between 80 – 120 West
TEMPO
Between 90 W and 110 W, there are nine owner operators of 30 satellites including older models still used in this location:
  Direct TV Group (7)
  AGS (5)
  Intelsat (5)
  Telesat (4)
  Hughes Network Systems (3)
  Echostar (2)
  SkyTerra (2)
  Inmarsat (1)
  ICO Global Communications (1)
(typical)
Notes: The atmospheric instruments can accomplish their science objectives in orbit locations from around 110 W to 90 W
The ocean science instrument needs to be in an orbit location between 85 W to 95 W to accomplish its science objectives

## Slide 8: The view from GEO

## Slide 9: TEMPO hourly NO2 sweep
N.B. special
operations!

## Slide 10: Los Angeles coverage
Every hour!

## Slide 11: Mexico City coverage
¡Cada hora!

## Slide 12: Science studies
  Spatial resolution: allow tracking pollution at sub-urban scale
    GEO at 100°W: 2.1 km N/S × 4.7 km E/W = 9.8 km2 (native) at center of FOR (36.5°N, 100°W)
    Full resolution for NO2, HCHO, total O3 products
    Co-add 4 N/S pixels for O3 profile product: 8.4 km N/S × 4.7 km E/W
~ 1/300 of GOME-2
~ 1/30 of OMI

## Slide 13: www.epa.gov/rsig
TEMPO will use the EPA’s Remote Sensing Information Gateway (RSIG) for subsetting, visualization, and product distribution – to make TEMPO YOUR instrument

## Slide 14: Data products, science studies (the Green Paper), special operations
Volcanic SO2 (column amount and plume altitude is a potential research product.
Diurnal out-going shortwave radiation and cloud forcing is a potential research product.
Additional cloud/aerosol products are possible using the O2-O2 collision complex and/or the O2 B band.
Yet more aerosol products will combine measurements from TEMPO and GOES-R.
Nighttime “city lights” products, which represent anthropogenic activities at the same spatial resolution as air quality products, may be produced twice per day (late evening and early morning) as a research product. Meeting TEMPO measurement requirements for NO2 (visible) implies the sensitivity for city lights products over the CONUS within a 2-hour period at 2×4.5 km2 to 1.1×10-8 W cm-2 sr-1 μm-1.
Several additional first-measurement molecules are being studied.
H2O will be produced at launch from the 7ν vibrational polyad at 445 nm. Water vapor retrieved from the visible spectrum has good sensitivity to the planetary boundary layer, since the absorption is optically thin, and is available over both the land and ocean. The hourly coverage of TEMPO will greatly improve the knowledge of water vapor’s diurnal cycle and make rapid variations in time readily observed.

## Slide 15: Clouds and aerosols
Clouds The launch cloud algorithm is be based on the rotational Raman scattering (RRS) cloud algorithm that was developed for OMI by GSFC. Retrieved cloud pressures from OMCLDRR are not at the geometrical center of the cloud, but rather at the optical centroid pressure (OCP) of the cloud.
Aerosols TEMPO’s launch algorithm for retrieving aerosols will be based upon the OMI aerosol algorithm that uses the sensitivity of near-UV observations to particle absorption to retrieve Absorbing Aerosol Index (AAI), aerosol optical depth (AOD) and single scattering albedo (SSA). TEMPO may be used together with the advanced baseline imager (ABI) instruments on the NOAA GOES-R and GOES-S satellites for aerosol retrievals, reducing AOD and fine mode AOD uncertainties from 30% to 10% and from 40% to 20%.

## Slide 16: NOx studies
Lightning NOx Interpretation of satellite measurements of tropospheric NO2 and O3, and upper tropospheric HNO3 lead to an overall estimate of 6 ± 2 Tg N y-1 from lightning [Martin et al., 2007]. TEMPO measurements, including tropospheric NO2 and O3, can be made for time periods and longitudinal bands selected to coincide with large thunderstorm activity, including outflow regions, with fairly short notice.
Soil NOx Jaeglé et al. [2005] estimate 2.5 - 4.5 TgN y-1 are emitted globally from nitrogen-fertilized soils, still highly uncertain. The US a posteriori estimate for 2000 is 0.86 ± 1.7 TgN y-1. For Central America it is 1.5 ± 1.6 TgN y-1. They note an underestimate of NO release by nitrogen-fertilized croplands as well as an underestimate of rain-induced emissions from semiarid soils.
TEMPO is able to follow the temporal evolution of emissions from croplands after fertilizer application and from rain-induced emissions from semi-arid soils. Should higher than hourly temporal resolution over selected regions be useful, that may be accomplished by special observations. It has also been noted by Martin et al. [2000] that improved constraints on soil NOx emissions may also improve estimated of lightning NOx emissions.

## Slide 17: Halogens
BrO will be produced at launch, assuming stratospheric AMFs. Scientific studies will correct retrievals for tropospheric content. IO was first measured from by SAO space using SCIAMACHY spectra [Saiz-Lopez et al., 2007]. It will be produced as a scientific product, particularly for coastal studies, assuming AMFs appropriate to lower tropospheric loading.
The atmospheric chemistry of halogen oxides over the ocean, and in particular in coastal regions, can play important roles in ozone destruction, oxidizing capacity, and dimethylsulfide oxidation to form cloud-condensation nuclei [Saiz-Lopez and von Glasow, 2012]. The budgets and distribution of reactive halogens along the coastal areas of North America are poorly known. Therefore, providing a measure of the budgets and diurnal evolution of coastal halogen oxides is necessary to understand their role in atmospheric photochemistry of coastal regions. Previous ground-based observations have shown enhanced levels (at a few pptv) of halogen oxides over coastal locations with respect to their background concentrations over the remote marine boundary layer [Simpson et al., 2015]. Previous global satellite instruments lacked the sensitivity and spatial resolution to detect the presence of active halogen chemistry over mid-latitude coastal areas. TEMPO observations together with atmospheric models will allow examination of the processes linking ocean halogen emissions and their potential impact on the oxidizing capacity of coastal environments of North America.
TEMPO also performs hourly measurements one of the world’s largest salt lakes: the Great Salt Lake in Utah. Measurements over Salt Lake City show the highest concentrations of BrO over the globe. Hourly measurement at a high spatial resolution can improve understanding of BrO production in salt lakes.

## Slide 18: Spectral indicators
Fluorescence and other spectral indicators Solar-induced fluorescence (SIF) from chlorophyll over both land and ocean will be measured. In terrestrial vegetation, chlorophyll fluorescence is emitted at red to far-red wavelengths (~650-800 nm) with two broad peaks near 685 and 740 nm, known as the red and far-red emission features. Oceanic SIF is emitted exclusively in the red feature. SIF measurements have been used for studies of tropical dynamics, primary productivity, the length of carbon uptake period, and drought responses, while ocean measurements have been used to detect red tides and to conduct studies on the physiology, phenology, and productivity of phytoplankton. TEMPO can retrieve both red and far-red SIF by utilizing the property that SIF fills in solar Fraunhofer and atmospheric absorption lines in backscattered spectra normalized by a reference (e.g., the solar spectrum) that does not contain SIF.
TEMPO will also be capable of measuring spectral indices developed for estimating foliage pigment contents and concentrations. Spectral approaches for estimating pigment contents apply generally to leaves and not the full canopy. A single spectrally invariant parameter, the Directional Area Scattering Factor (DASF), relates canopy-measured spectral indices to pigment concentrations at the leaf scale.
UVB TEMPO measurements of daily UV exposures build upon heritage from OMI and TROPOMI measurements. Hourly cloud measurements from TEMPO allow taking into account diurnal cloud variability, which has not been previously possible. The OMI UV algorithm is based on the TOMS UV algorithm. The specific product is the downward spectral irradiance at the ground (in W m-2 nm-1) and the erythemally weighted irradiance (in W m-2).

## Slide 19: Traffic, biomass burning
Morning and evening higher-frequency scans The optimized data collection scan pattern during mornings and evenings provides multiple advantages for addressing TEMPO science questions. The increased frequency of scans coincides with peaks in vehicle miles traveled on each coast.
Biomass burning The unexplained variability in ozone production from fires is of particular interest. The suite of NO2, H2CO, C2H2O2, O3, and aerosol measurements from TEMPO is well suited to investigating how the chemical processing of primary fire emissions effects the secondary formation of VOCs and ozone. For particularly important fires it is possible to command special TEMPO observations at even shorter than hourly revisit time, probably as short as 10 minutes.

## Slide 20: City lights
SNRs of various artificial lighting types normalized to a common VIIRS-DNB response with a 10s dwell, no co-addition, and no spatial binning, assuming a dark current of 2800 e- s-1. City lights over all of greater North America can either be observed piecemeal over several days or in a single scan near the winter solstice.

## Slide 21: Air quality and health
TEMPO’s hourly measurements allow better understanding of the complex chemistry and dynamics that drive air quality on short timescales. The density of TEMPO data is ideally suited for data assimilation into chemical models for both air quality forecasting and for better constraints on emissions that lead to air quality exceedances. Planning is underway to combine TEMPO with regional air quality models to improve EPA air quality indices and to directly supply the public with near real time pollution reports and forecasts through website and mobile applications. As a case study, an OSSE for the Intermountain West was performed to explore the potential of geostationary ozone measurements from TEMPO to improve monitoring of ozone exceedances and the role of background ozone in causing these exceedances (Zoogman et al. 2014).

## Slide 22: The end! Thanks to NASA, ESA, Ball Aerospace & Technologies Corp., The Boeing Company

## Slide 23: Backups

## Slide 24: Team TEMPO!

## Slide 25
Team Member | Institution | Role | Responsibility
K. Chance | SAO | PI | Overall science development; Level 1b, H2CO, C2H2O2
X. Liu | SAO | Deputy PI | Science development, data processing; O3 profile, tropospheric O3
J. Al-Saadi | LaRC | Deputy PS | Project science development
J. Carr | Carr Astronautics | Co-I | INR Modeling and algorithm
M. Chin | GSFC | Co-I | Aerosol science
R. Cohen | U.C. Berkeley | Co-I | NO2 validation, atmospheric chemistry modeling, process studies
D. Edwards | NCAR | Co-I | VOC science, synergy with carbon monoxide measurements
J. Fishman | St. Louis U. | Co-I | AQ impact on agriculture and the biosphere
D. Flittner | LaRC | Project Scientist | Overall project development; STM; instrument cal./char.
J. Herman | UMBC | Co-I | Validation (PANDORA measurements)
D. Jacob | Harvard | Co-I | Science requirements, atmospheric modeling, process studies
S. Janz | GSFC | Co-I | Instrument calibration and characterization
J. Joiner | GSFC | Co-I | Cloud, total O3, TOA shortwave flux research product
N. Krotkov | GSFC | Co-I | NO2, SO2, UVB
M. Newchurch | U. Alabama Huntsville | Co-I | Validation (O3 sondes, O3 lidar)
R.B. Pierce | NOAA/NESDIS | Co-I | AQ modeling, data assimilation
R. Spurr | RT Solutions, Inc. | Co-I | Radiative transfer modeling for algorithm development
R. Suleiman | SAO | Co-I, Data Mgr. | Managing science data processing, BrO, H2O, and L3 products
J. Szykman | EPA | Co-I | AIRNow AQI development, validation (PANDORA measurements)
O. Torres | GSFC | Co-I | UV aerosol product, AI
J. Wang | U. Nebraska | Co-I | Synergy w/GOES-R ABI, aerosol research products
J. Leitch | Ball Aerospace | Collaborator | Aircraft validation, instrument calibration and characterization
D. Neil | LaRC | Collaborator | GEO-CAPE mission design team member
TEMPO Science Team, U.S.

## Slide 26
Team Member | Institution | Role | Responsibility
Randall Martin | Dalhousie U. | Collaborator | Atmospheric modeling, air mass factors, AQI development
Chris McLinden | Environment Canada | Collaborator | Canadian air quality coordination
Michel Grutter de la Mora | UNAM, Mexico | Collaborator | Mexican air quality coordination
Gabriel Vazquez | UNAM, Mexico | Collaborator | Mexican air quality, algorithm physics
Amparo Martinez | INECC, Mexico | Collaborator | Mexican environmental pollution and health
J. Victor Hugo Paramo Figeuroa | INECC, Mexico | Collaborator | Mexican environmental pollution and health
Brian Kerridge | Rutherford Appleton Laboratory, UK | Collaborator | Ozone profiling studies, algorithm development
Paul Palmer | Edinburgh U., UK | Collaborator | Atmospheric modeling, process studies
Alfonso Saiz-Lopez | CSIC, Spain | Collaborator | Atmospheric modeling, process studies
Juan Carlos Antuña Marrero | GOAC, Cuba | Collaborator | Cuban Science team lead, Cuban air quality
Osvaldo Cuesta | GOAC, Cuba | Collaborator | TEMPO validation, Cuban air quality
René Estevan Arredondo | GOAC, Cuba | Collaborator | TEMPO validation, Cuban air quality
J. Kim | Yonsei U. | Collaborators, Science Advisory Panel | Korean GEMS, CEOS constellation of GEO pollution monitoring
C.T. McElroy | York U. Canada |  | CSA PHEOS, CEOS constellation of GEO pollution monitoring
B. Veihelmann | ESA |  | ESA Sentinel-4, CEOS constellation of GEO pollution monitoring
J.P. Veefkind | KNMI |  | ESA Sentinel-5P (TROPOMI)
TEMPO Science Team, non-U.S.

## Slide 27: Why the Smithsonian?
Langley, S.P., and C.G. Abbot, Annals of the Astrophysical Observatory of the Smithsonian Institution, Volume 1 (1900).
Langley’s recently invented bolometer was used to make measurements from the infrared through the near ultraviolet in order to determine the mean value of the solar constant and its variation. Langley and Abbot also developed substantial new experimental techniques (such as an early chart recorder) and various analysis techniques (e.g., the “Langley plot”), including photographic techniques for high and low pass filtering to produce line spectra from “bolographs” (spectra), illustrated, foreshadowing the high pass filtering used today by researchers employing the DOAS technique for analyzing atmospheric spectra.

## Slide 28: TEMPO instrument project detailed organization structure
TEMPO Instrument
Principal Investigator: Kelly Chance
Deputy Principal Investigator: Xiong Liu
Program Administrator: Joseph Webber
Investigation Advisory Panel
SAO, LaRC, Ball Senior Management
Project Management
Project Manager: Wendy Pennington
Project Scientist: David Flittner
Deputy Project Scientist: Jay Al-Saadi
Deputy PM: Craig Jones, COR
Deputy PP&C: Don Shick
Instrument
PM Dennis Nicks
Chief SE: Laura Hale
Instrument Performance: Brian Baker
Systems Engineering
Project CE: David Rosenbaum
SE: Mark Andraschko
Safety & Mission Assurance
Mission Assurance Manager: Jose Caraballo
Science Team
Instrument Operations
John E. Davis
Science Advisory Panel
Geo Constellation/CEOS
Ground
Systems
Raid M. Suleiman
Science Data Processing System
John Houck
Management Support
Schedules: Barbara Guilmette
Configuration Manager: Donna Lewis
Communications: Jonathan Behun/Katie Bethea

## Slide 29
Why geostationary? High temporal and spatial resolution
Hourly NO2 surface concentration and integrated column calculated by CMAQ air quality model: Houston, TX, June 22-23, 2005
June 22
Hour of Day (UTC)
June 23
LEO observations provide limited information on rapidly varying emissions, chemistry, & transport
GEO will provide observations at temporal and spatial scales highly relevant to air quality processes

## Slide 30: Instrument layout
Calibration Mechanism Assembly
Telescope Assembly
Spectrometer Assembly
Scan Mechanism Assembly
Focal Plane
Assembly
Focal Plane Electronics
Instrument Support
Assembly
Radiator Assembly
Instrument
Control Electronics
Notes: Most of final drawings done; detectors in-house; grating ordered; optical bench ordered

## Slide 31: A day in the life
Figure 7. Nominal daily operations for TEMPO instrument.

## Slide 32: TEMPO footprint (GEO at 100º W)
For GEO at 80ºW, pixel size at 36.5ºN, 100ºW is 2.2 km × 5.2 km.
Location | N/S (km) | E/W (km) | GSA (km2)
36.5oN, 100oW | 2.11 | 4.65 | 9.8
Washington, DC | 2.37 | 5.36 | 11.9
Seattle | 2.99 | 5.46 | 14.9
Los Angeles | 2.09 | 5.04 | 10.2
Boston | 2.71 | 5.90 | 14.1
Miami | 1.83 | 5.04 | 9.0
Mexico City | 1.65 | 4.54 | 7.5
Canadian tar sands | 3.94 | 5.05 | 19.2
Assumes 2000 N/S pixels |  |  | 

## Slide 33: Global pollution monitoring constellation
Sentinel-5P
(once per day)
TEMPO
(hourly)
Sentinel-4
(hourly)
GEMS
(hourly)
Courtesy Jhoon Kim,
Andreas Richter
Policy-relevant science and environmental services enabled by common observations
Improved emissions, at common confidence levels, over industrialized Northern Hemisphere
Improved air quality forecasts and assimilation systems
Improved assessment, e.g., observations to support United Nations Convention on Long Range Transboundary Air Pollution
80-115°W
0°
2021+ launch
128.2°E
2019 launch

## Slide 34: Bay Area coverage
Every hour!

## Slide 35: Optical depths for typical GEO measurement geometry
Best fitting to date:
2.0×10-4 full-scale radiance
(Instrument vs. algorithm: Tied! S/N drives instrument if meas. requirements can be met
Important!

## Slide 36: Oversampling Lei Zhu et al., 2014

## Slide 37: Oversampling

## Slide 38: XL ozone profile retrievals
Retrieval averaging kernels based on iterative nonlinear retrievals from synthetic TEMPO radiances with the signal to noise ratio (SNR) estimated using the TEMPO SNR model at instrument critical design review in June 2015 for (a) UV (290-345 nm) retrievals and (b) UV/Visible (290-345 nm, 540-650 nm) retrievals for clear-sky condition and vegetation surface with solar zenith angle 25°, viewing zenith angle 45° and relative azimuthal angle 86°. DFS is degrees of freedom for signal, the trace of the averaging kernel matrix, which is an indicator of the number of pieces of independent information in the solution.

## Slide 39: OSSE for the Intermountain West Zoogman et al., 2014
Longitude-altitude cross-section of ozone concentrations (36oN, 3 GMT on June 14, 2010) associated with a stratospheric intrusion. The “true” state from an independent chemical transport model (top left) is compared to the GEOS-Chem model without data assimilation (top right) and with assimilation of TEMPO data (bottom). Local topography is shown in white.

## Slide 40: GOME, SCIAMACHY, and OMI measurement examples
Kilauea activity, source of the VOG event in Honolulu on 9 November 2004
O3 strat
trop
CHOCHO
HCHO

## Slide 41: TEMPO summary
Currently on-schedule and on-budget
  Passed System Requirements Review and Mission Definition Review in November 2013
  Passed KDP-B April 2014
  Most technical issues solved at the preliminary design level, following technical interchange meeting at Ball, April 2014
  Passed PDR on July 31, 2014
  Now in Phase C: KDP-C April 10, 2015
  Instrument CDR June 2015
  Ground Systems CDR March 2016
Select satellite host 2017+
  TEMPO operating longitude and launch date are not known until after host selection
Instrument delivery 05/2017 for launch 11/2018 or later

## Slide 42
The Rules
Don’t define your algorithm in advance
  Test all steps for utility and applicability
  Let the physics guide you
No black boxes
  You must have and understand all source code, and be able to modify it as necessary
  You must test all assumptions
Fitters must go to bedrock: (Occam’s taser): If you didn’t do it yourself, it isn’t done (and you have to do it down to bedrock and also understand and publish all the reasons why you did it that way)
Reference data as used must be peer-reviewed, published, and publicly-available (P3)
No unexplained shifts in cross sections, for example
A description of the analysis as performed must be publicly available.
Ecclesiastes 11:1Cast thy bread upon the waters: for thou shall find it after many days.